## Slide 1: Coexistence Study of Different Medium Access Mechanisms Using a Software Defined Radio Testbed
Bachelor Thesis Talk
Alexander Pastor - December 18th, 2017
Notes: Master slide:
Welcome audience to bachelor thesis presentation XMAS-Edition "Coexistence Study of Different Medium Access Mechanisms Using a Software Defined Radio Testebed"

## Slide 2
Motivation
Contents
Results and Conclusions
Methodology
Notes: Contents:
Throughout the course of this presentation we will:
Motivate the thesis, i.e. what lead to the work and what was done
Describe the methodology, i.e. which devices an d software was used, the measurement setup and scenarios, the automatic script system to capture the results
Talk about the results and interpret them

## Slide 3: Motivation
Motivation
Demand for high transfer rates
Network Densification
Intertechnological Coexistence
⇒ Need to design good MAC protcols
Notes: Motivation I:
Network Densification, e.g. shopping mall or resturants, IoT, industry 4.0
Intertechnological Coexistence: Bluetooth, Wi-Fi, ZigBee, LTE in unlicensed bands
Theoretical Insights: Difference in performance of contention-based MAC protocols

## Slide 4: Motivation
Motivation
Design Drivers
Maximize
- Throughput
- Coverage
- Security
- Flexibility
Minimize
- Latency
- Jitter
- Power Consumption
- Complexity
Operating Conditions
- Intertechnological Coexistence
- Traffic Patterns
- Directional Traffic
Challenges Wireless MAC
- Interference
- Hidden Node Problem
- Exposed Node Problem
- Security
- Power Supply
Why is it hard to design good MAC protocols?
⇒ Protocol design has to be confined/focussed on certain aspects depending on the application
Notes: Motivation II - why is it hard to design good MAC protocols:
Design Criteria
  Apart from the most obvious design criteria of maximizing throughput and minimizing latency...
  Jitter in terms of first-order derivative of latency has to be low for some real-time applications
  Flexibility in terms of adapting to new situations, e.g. varying traffic load
  Power efficiency is important for devices that use battery as means of power supply (mention influence of physical layer => [spectral efficiency] = bits/W/Hz)
  Complexity => bad predicatability, complicated mathematical models of performance aspects if any => motivation to use software defined radio
Overabundance of design criteria that are contradictory
  power versus coverage (high TX power = high power consumption)
  latency versus throughput (p-persistent CSMA)
  throughput versus complexity (ALOHA)
  security versus flexibility:
Challenges for wireless MAC
  Wireless => Propagation in all directions around the origin => hidden / exposed node problem (hidden node problem = node cannot be heard by sender, but can interfere with transmission, exposed node problem = sender refrains from sending although exposed node cannot interfere with transmission in the region between recevier and sender ==> backup slides)
  Related: Interference caused by hidden node problem / technologies without LBT
  Security: low power signal jamming => reducing throughput and battery life

## Slide 5: Motivation
Motivation
Some MAC Mechanisms
Carrier Sensing
- Thresholding
- Preamble Sampling
- Outlier Detection
Random Backoff
- Minimium CW
- CW Growth
Coordinator
- Time Domain
- Frequency Domain
- Code Domain
Protcol Classification
Handshaking
- Timeouts
- Acknowledgments
- RTS/CTS Exchange
- Sliding Windows
Notes: Classification of Mechanisms:
Classification of MAC Protocols
Duty cycling can be used as a power saving mechanism in WSN MAC protocols or as a coexistence mechanism for LTE in the unlicensed bands (LTE-U).

## Slide 6
Methodology
Transmitter 1
Receiver
Transmitter 2
Protocol A
Parameter 1
Parameter 2
Parameter 3
Protocol B
Parameter 1
Parameter 2
Parameter 3
Scenarios
same MAC scenarios
different MAC scenarios
baseline vs. coexistence
SDR, GNU Radio
USRPs: NI 2920, Ettus Research USRP2
Notes: Devices
  Two NI 2920 and two Ettus Research USRP2s
  Receiver-Sender Pairs called links
  Sniffer
Measurement Script system
  File Management: Config files, Log files

## Slide 7
Methodology
automated measurement procedure
modular design principle
file management
GNU Radio flowgraphs
data processing & plotting

## Slide 8
Cat the logs
2
1
3
1 [meow@catcondo ~]$ cat log
2 [meow@catcondo ~]$ tail -n +17 log
3 [meow@catcondo ~]$ tail -n 150 log
3 [meow@catcondo ~]$ cat log $(python belated_evaluation.py &> log)
file management
measurement
data processing & plotting
log is the path to the log file

## Slide 9
Results
Pure ALOHA x2
Transmitter 1
Receiver
Transmitter 2
ALOHA
pure
saturated
ALOHA
pure
saturated
Expectations:
Collisions
No throughput
100% packet loss

## Slide 10
Results
Same MAC protocol on the two links - Pure ALOHA
⇒ 0 throughput.
max. ≈ 135 kbps
collisions!
timeout 200ms

## Slide 11
Results
Same MAC protocol on the two links - Pure ALOHA
⇒ 100% packet loss

## Slide 12
Results
CSMA/CA (high parameter values) x2
Transmitter 1
Receiver
Transmitter 2
CSMA/CA
DIFS = 15 ms
SIFS = 3 ms
BO = 6 ms
saturated
CSMA/CA
DIFS = 15 ms
SIFS = 3 ms
BO = 6 ms
saturated
Expectations:
Few Collisions
Mediocore,
evenly distributed throughput
Low packet loss

## Slide 13
Results
Same MAC protocol on the two links - CSMA/CA high parameter values
Sniffer energy plot
distinct power levels
long idle periods due to backoff
negative impact on throughput
Logical channel occupation
data frames transmitter POV
ack frames receiver POV

## Slide 14
Results
Same MAC protocol on the two links - CSMA/CA high parameter values
Baseline throughput only about a third of ALOHA
Coexistence throughput roughly halves compared to baseline

## Slide 15
Results
CSMA/CA (low parameter values) x2
Transmitter 1
Receiver
Transmitter 2
CSMA/CA
DIFS = 5 ms
SIFS = 1 ms
BO = 2 ms
saturated
CSMA/CA
DIFS = 5 ms
SIFS = 1 ms
BO = 2 ms
saturated
Expectations:
Some collisions
High channel utilization
High, evenly distributed throughput
Low packet loss

## Slide 16
Results
Same MAC protocol on the two links - CSMA/CA low parameter values
Types of collisions
"granularity type"
"1-persistent type"
Throughput expectations met!
80 kbps baseline
≈ halves in coexistence

## Slide 17
Results
Same MAC protocol on the two links - CSMA/CA low parameter values
Backoff 55-60 s per 100 s
close to ideal backoff duration

## Slide 18
Results
1-persistent CSMA x2
Transmitter 1
Receiver
Transmitter 2
1-p CSMA
DIFS = 15 ms
SIFS = 0 ms
BO = 0 ms
saturated
1-p CSMA
DIFS = 15 ms
SIFS = 0 ms
BO = 0 ms
saturated
Expectations:
Lots of collisions
Very high channel utilization
Capture effect

## Slide 19
Results
Same MAC protocol on the two links - 1-persistent CSMA
high SINR versus low SINR

## Slide 20
Results
unsaturated ALOHA + CSMA/CA (high parameters)
Transmitter 1
Receiver
Transmitter 2
ALOHA
pure
unsaturated
interval T ~ exp(λ=1/200ms)
CSMA/CA
DIFS = 15 ms
SIFS = 3 ms
BO = 6 ms
saturated
Expectations:
Some collisions
Low channel utilization
Low throughput

## Slide 21
Results
Different MAC protocol on the two links - unsaturated ALOHA + CSMA/CA

## Slide 22
Results
Different MAC protocol on the two links - unsaturated ALOHA + CSMA/CA
LBT
versus
no LBT

## Slide 23
Results
2x CSMA/CA (high+low)
Transmitter 1
Receiver
Transmitter 2
CSMA/CA
DIFS = 5 ms
SIFS = 1 ms
BO = 2 ms
saturated
CSMA/CA
DIFS = 15 ms
SIFS = 3 ms
BO = 6 ms
saturated
Expectations:
Some collisions
Low channel utilization
Low throughput

## Slide 24
Results
Different MAC protocol on the two links - different CSMA/CA variants
Backoff (slot) duration decisive factor in channel share...
... and thus throughput

## Slide 25
Conclusions
Even low loads of ALOHA have strong, negative impact on all other nodes within reach.
The LBT mechanism of CSMA/CA enables fair (almost) collision-free traffic.
CSMA/CA parameter have a major impact on the performance
  High values ⇒ excessive idle periods
  Low values ⇒ below time granularity
  SIFS = 0, BO = 0, DIFS ≠ 0 ⇒ 1-persistent CSMA
  Random backoff is the decisive factor in transmission cycle
Capture effect

## Slide 26
Q&A Time!
Notes: Contents:
Throughout the course of this presentation we will:
Motivate the thesis, i.e. what lead to the work and what was done
Describe the methodology, i.e. which devices an d software was used, the measurement setup and scenarios, the automatic script system to capture the results
Talk about the results and interpret them

## Slide 27
Backup Slides

## Slide 28: Motivation
Motivation
Security Aspects in MAC Design
Targetting: service availability and data integrity
Example attack against S-MAC: Bogus SYNC packets to keep clusters awake
Denial of Sleep Attack
Interrogation Attack
Attacker: Repeated RTS to target neighborhood node
Notes: Other target: confidentiality

## Slide 29
Methodology
Testbed Setup Parameters

## Slide 30
Methodology
Sender (ALOHA) Flowgraph

## Slide 31
Methodology
Sender (CSMA) Flowgraph

## Slide 32
Methodology
Sniffer+Receiver Flowgraph

## Slide 33
Results
Same MAC protocol on the two links - CSMA/CA with medium parameter values

## Slide 34
Results
Same MAC protocol on the two links - CSMA/CA with medium parameter values

## Slide 35
Results
Different MAC protocol on the two links - saturated ALOHA + CSMA/CA

## Slide 36
Results
Different MAC protocol on the two links - 1-persistent CSMA/CA + unsat. ALOHA

## Slide 37
Results
Different MAC protocol on the two links - 1-persistent CSMA/CA + unsat. ALOHA

## Slide 38
Results
Different MAC protocol on the two links - 1-persistent CSMA/CA + unsat. CSMA/CA

## Slide 39
Results
Different MAC protocol on the two links - 1-persistent CSMA/CA + unsat. CSMA/CA